## Slide 1: Lecture 3.5. I/O and Interface
Haonan Wang
CMPE 200 Computer Architecture & Design

## Slide 2: Computer Architecture Overview
Software/Applications
Processor
Operating System
Instruction Set
Architecture
Firmware
Compiler
Registers
Cache
Memory
HDD/SSD
ISA & Processor
Memory Hierarchy
I/O Interface

## Slide 3: Peripheral Devices
Device | Behavior | Partner | Protocol | Data rate (Mb/sec)
Keyboard | input | human | USB, PS/2 | 0.0001
Mouse | input | human | USB, PS/2 | 0.0038
Laser printer | output | human | Parallel Port | 3.20
Graphics display | output | human | DP, HDMI | 8000-80000
Graphics card | accelerator | machine | PCIE | 2000-8000
Network/LAN | input or output | machine | TCP/IP | 10-10000
Magnetic disk | storage | machine | SATA | 240-2560
Solid state drive | storage | machine | SATA, PCIE | 4000-28000
9 orders of magnitude range

## Slide 4: I/O Performance Measures
I/O bandwidth (throughput)
  How much data can we move through the system in a certain time?
  How many I/O operations can we do per unit time?
I/O response time (latency)
  The total elapsed time to accomplish an input or output operation
  Especially important in real-time systems
Many applications require both high throughput and short response times
Both performance and fairness matters!

## Slide 5: A Typical I/O System
Processor
Memory - I/O Bus
Network
Interrupts
Cache
Main
Memory
I/O
Controller
Disk
I/O
Controller
I/O
Controller
Graphics
Disk
To interface a peripheral device with a processor, an interface wrapper (e.g., controller) is needed
Important factors:
Performance
Expandability
Resilience
…

## Slide 6: Interface Wrappers
Contains registers to hold signals (control, data, and status) that communicate between the peripheral device and the processor
  memory mapped: each interface register can be accessed via an address
The interface wrapper usually contains additional logics (such as address decoder)
  If the interface protocol is more complicated, the interface wrapper will also contain control unit (FSM)

## Slide 7: Processor Interface Mechanisms
Two ways for processors to access peripheral devices:
  Port-mapped I/O (PMIO): isolated I/O, special I/O instructions, separate address spaces, time shared bus
  Memory-mapped I/O (MMIO): one address space
MIPS processors use memory-mapped I/O
  Use load and store instructions to communicate with peripheral devices
  For a MIPS processor that only supports lw and sw, all data transfer will be 32 bits

## Slide 8: Processor Interface Mechanisms
Two ways to communicate with CPU:
  Polling: The CPU polls the device periodically.
    Simple but time consuming
  Interrupt: The I/O device calls the CPU actively
    Fast but complex: which interrupt has high priority?
Two ways for data transfer between the memory and I/O:
  CPU controlled
  Direct Memory Access (DMA)

## Slide 9: Memory-Mapped I/O Datapath

## Slide 10: Memory-Mapped I/O Example
Base Address | Address Range | R/W | Description
0x00000000 | 0x00 – 0xFC | R/W | Data Memory
0x00000800 | 0x00 – 0x0C | R/W | Device 1
0x00000900 | 0x00 – 0x0C | R/W | Device 2
System Integration Memory Map
0xFC = 11111100  64 (0x00 – 0x3F) word addresses
0x0C = 00001100  4 (0x00 – 0x03) word addresses
Last two bits are byte offsets

## Slide 11: Factorial Accelerator Wrapper
Assignment1

## Slide 12: Factorial Accelerator Interface Registers
Address | R/W | Register Name | Bits | Bit Definition
00 | R/W | Data Input (n) | 31:4 | Unused
 |  |  | 3:0 | Input Data, n[3:0]
01 | R/W | Control Input (Go) | 31:1 | Unused
 |  |  | 0 | Go bit
10 | R | Control Output (Done, Err) | 31:2 | Unused
 |  |  | 1 | Err bit
 |  |  | 0 | Done bit
11 | R | Data Output (Result) | 31:0 | Result Data, nf[31:0]

## Slide 13: Factorial Accelerator Interface (1)
The factorial accelerator’s local address decoder module:

## Slide 14: Factorial Accelerator Interface (2)
Registers for inputs n, Go, and output Result:

## Slide 15: Factorial Accelerator Interface (3)
Registers for status signals Done, and Err:

## Slide 16: Factorial Accelerator Interface (4)
Read Data Logic (the output MUX):

## Slide 17: General Purpose I/O (GPIO) Wrapper

## Slide 18: GPIO Memory-Mapped Registers
Address | R/W | Register Name | Bits | Bit Definition
00 | R | Input 1 | 31:0 | General Input
01 | R | Input 2 | 31:0 | General Input
10 | R/W | Output 1 | 31:0 | General Output
11 | R/W | Output 2 | 31:0 | General Output

## Slide 19: MIPS Driver Code

## Slide 20: Midterm Exam Composition
Multiple-choice Single-answer: 4 points * 8 = 32
Multiple-choice Multiple-answer: 6 points (wrong or missing option -3) * 4 = 24
True or False: 3 points * 8 = 24
Questions & Answers: 10 points (steps 8 + answer 2) * 2 = 20
Bonus question: 10 points * 1 = 10
Total = 32 + 24 + 24 + 20 + 10 = 100 + 10
  If you get more than 100 points, the excessive points will be used to improved your overall grade.
Exam settings:
  Time: Thursday, Oct. 12, 15:00 - 16:15 @ ENG 331 (in-person only) with LockDown Browser
  Closed book (but you can print out the MIPS data card and use it if needed)
  Cheat sheet (handwritten): A4 paper * 1 allowed, pictures of both sides must be submitted before the exam
  Use of calculator and scratch paper allowed
  Double-check your laptop and turn off your cellphone before the exam